## Slide 1: DEVELOPMENT OF AN INSTRUMENTATION SYSTEM FOR THE CHARACTERISATION OF VELOSTAT MATERIAL
Examiner: Martin Ekström
Supervisors: Saad Abdullah, Abdelakram Hafid
Louis de Looze

## Slide 2: Velostat?
Introduction
Notes: Who has heard about Velostat except my supervisor?
Carbon impregnated polyethylene
Used for ESD safe packaging
Also used for sensors
Image: https://www.adafruit.com/product/1361

## Slide 3
Introduction
Notes: – sleep monitoring (e.g.,[1]);
– posture monitoring (e.g.,[2], [3]);
– floor‐based foot pressure measuring (e.g.,[4]);
– shoe insole pressure measuring (e.g.,[5], [6]);
– interactive sensing floors (e.g.,[7]);
– Musical Instrument Digital Interface (MIDI) controllers (e.g.,[8]).

## Slide 4: Instrumentation system?
Introduction
Notes: Why instrumentation system?
Researchers always build test sustem from zero → time and resource consuming
Sometimes no technical knowledge
Insturementation system should be used by everybody

## Slide 5: Current State
Background
Notes: How velostat?
Looking at current literature of velostat based tactile sensors
2 distinct methods: borders and velostat matrix
one uses the complete sheet as a sensor, other divides the sheet in multiple sensors
We will focus on border based sensors
Y. Zhang, G. Laput, and C. Harrison, “Electrick: Low-cost touch sensing using electric field tomography,” 2017. [Online]. Available: http://dx.doi.org/10.1145/3025453.3025842
L. Yuan, H. Qu, and J. Li, “Velostat sensor array for object recognition,” IEEE Sensors Journal, vol. 22, pp. 1692–1704, 1 2022.

## Slide 6: Sensing Principles
Background
Direct Current
Youzhi Zhang et al.
Alternating Current
Yang Zhang et al.
Notes: When with the border system, a measurement pair and injecting pair of electrodes
The injecting signal can be AC or DC
Both methods extensively researched
Y. Zhang, G. Laput, and C. Harrison, “Electrick: Low-cost touch sensing using electric field tomography,” 2017. [Online]. Available: http://dx.doi.org/10.1145/3025453.3025842
Y. Zhang, Z. Lin, X. You, X. Huang, J. Ye, and H. Wu, “A position‐sensitive electronic skin
based on boundary potential projection theory,” Sensor Review, vol. 40, no. 1, pp. 130–140,
Jan. 2020, ıſſN: 0260‐2288. DOı: 10 . 1108 / SR - 10 - 2019 - 0243. [Online]. Available:
https://doi.org/10.1108/SR-10-2019-0243.

## Slide 7: Overview
Implementation and Design

## Slide 8: Sensor Material & Connection
Implementation and Design
Notes: Connections on pcb
Exposed pads
Copper tape and kapton

## Slide 9: Instrumentation Hardware
Implementation and Design
Notes: 4 multiplexers
upper conencted to injecting signal
lower is connected to opamp
adc digitalises the signal
All mux pins connected to velostat

## Slide 10: Multiplexers
Implementation and Design
Notes: Here we can see the custom pcb with muxes

## Slide 11: Overview
Implementation and Design

## Slide 12: Web Visualisation
Implementation and Design
Notes: Single mode
Check velostat reaction
Enables us to change one parameter of the testing an evaluate quickly

## Slide 13: Web Visualisation
Implementation and Design
Notes: Sequencer mode

## Slide 14: Interaction flow
Implementation and Design

## Slide 15: Complete System
Results

## Slide 16: Single Mode
Results

## Slide 17: Sequencer Mode
Results

## Slide 18
Results
- video in folder -
Notes: Image: https://www.adafruit.com/product/1361

## Slide 19
Conclusion
Notes: Image: https://www.adafruit.com/product/1361

## Slide 20
Extra
Notes: Image: https://www.adafruit.com/product/1361

## Slide 21
Extra
Notes: Image: https://www.adafruit.com/product/1361

## Slide 22
Extra
Notes: Image: https://www.adafruit.com/product/1361